DLT (Direct Linear Transformation) based calibration

Image used for DLT:

Implementation steps:
Noted following 6 world points and correspoinding image points.

A matrix and results
[[144, 0, 144, 1, 0, 0, 0, 0, -68400, 0, -68400, -475], [0, 0, 0, 0, 144, 0, 144, 1, -463968, 0, -463968, -3222], [36, 0, 36, 1, 0, 0, 0, 0, -139464, 0, -139464, -3874], [0, 0, 0, 0, 36, 0, 36, 1, -85644, 0, -85644, -2379], [36, 72, 0, 1, 0, 0, 0, 0, -146304, -292608, 0, -4064], [0, 0, 0, 0, 36, 72, 0, 1, -18324, -36648, 0, -509], [72, 72, 0, 1, 0, 0, 0, 0, -233424, -233424, 0, -3242], [0, 0, 0, 0, 72, 72, 0, 1, -34200, -34200, 0, -475], [72, 0, 108, 1, 0, 0, 0, 0, -189864, 0, -284796, -2637], [0, 0, 0, 0, 72, 0, 108, 1, -216288, 0, -324432, -3004], [0, 0, 72, 1, 0, 0, 0, 0, 0, 0, -334224, -4642], [0, 0, 0, 0, 0, 0, 72, 1, 0, 0, -201600, -2800]]

Projection matrix is:
[[ -3.74192548e-03 -7.09352321e-04 -2.08639185e-03 9.11534249e-01]
 [ -1.19471698e-04 -4.38859509e-03 6.67848748e-04 4.11177210e-01]
 [ 1.03536464e-07 -2.21616919e-07 -3.72293950e-07 1.90809706e-04]]
camera intrinsic parameters are:
[[ -4.16539126e-03 4.99336916e-05 1.22688234e-03]
 [ 0.00000000e+00 4.14347407e-03 1.59739944e-03]
 [ -0.00000000e+00 0.00000000e+00 4.45462281e-07]]

camera extrinsic parameters are:
[[ 0.96537612 0.01336473 0.26051935]
 [-0.11843851 -0.86736175 0.48337969]
 [ 0.23242476 -0.49749873 -0.83574742]]
Image points calculated using this camera matrix:
World point: [144, 0, 144]
Actual Image point: [475, 3222]
Calculated point: [475.03257863145433, 3222.3254744639958]

World point: [36, 0, 36]
Actual Image point: [3874, 2379]
Calculated point: [3874.0001105728634, 2378.999782087476]

World point: [36, 72, 0]
Actual Image point: [4064, 509]
Calculated point: [4064.0000331347605, 508.99919994606785]

World point: [72, 72, 0]
Actual Image point: [3242, 475]
Calculated point: [3241.9999676195521, 475.00078370434977]

World point: [72, 0, 108]
Actual Image point: [2637, 3004]
Calculated point: [2636.9372499893252, 3003.3732202137849]

World point: [0, 0, 72]
Actual Image point: [4642, 2800]
Calculated point: [4642.0302193340867, 2800.3024597701519]

wireframe for the same:

ransac:

noted image coordinates for 20 points. Then followed following steps to calibrated:
1. Randomly select 6 points out of 20.
2. Find P matrix using above selected points using DLT.
3. Using this P matrix, Find out image coordinates (xi, yi) for all the 20 points.
4. Calculate the error in terms of Euclidean distance from calculated values to
actual values.
5. If this error is lesser than previously recorded error till now then select this P
matrix as the final result.
6. Repeat above 5 steps untill we reach threshold.

Points chosen:
x = [[4731, 2453], [4873,1407], [4914, 564], [4010, 2073], [4826, 2141], [4642, 2800], [3874, 2379], [3038,2304], [4037, 1325], [4064,509], [3242, 475], [2440,1216], [3731,2712],[1155,2460], [2637,3004], [836,2807], [475,3222], [897,333]]
X = [[0, 0, 36], [0,36,0], [0,72,0], [36,0,0], [0,0,0], [0,0,72], [36,0, 36], [72,0,36], [36,36,0], [36,72,0], [72,72,0],[108,36,0], [36,0,72], [140,0,72],[72,0,108],[144,0,108], [144,0,144], [180,72,0]]

threshold taken: 1

Projection matrix is:
[[ 3.96173182e-03 3.11538970e-04 1.86238666e-03 -9.13153168e-01]
 [ 1.87708116e-04 4.24084506e-03 -8.65777998e-04 -4.07569902e-01]
 [ -7.63671423e-08 1.19359844e-07 3.05929301e-07 -1.89856060e-04]]
camera intrinsic parameters are:
[[ 4.29469467e-03 3.63134684e-05 -9.02850295e-04]
 [ 0.00000000e+00 -4.27975669e-03 -6.73242439e-04]
 [ -0.00000000e+00 0.00000000e+00 -3.37151969e-07]]

camera extrinsic parameters are:
[[ 0.9707605 0.00602357 0.23997451]
 [-0.07949096 -0.93521699 0.34503677]
 [ 0.22650659 -0.35402387 -0.9073929 ]]
Image points calculated using this camera matrix:
World point: [0, 0, 36]
Actual Image point: [4731, 2453]
Calculated point: [4731.0161099567049, 2453.2068787532053]

World point: [0, 36, 0]
Actual Image point: [4873, 1407]
Calculated point: [4860.6494406681559, 1373.6834889940335]

World point: [0, 72, 0]
Actual Image point: [4914, 564]
Calculated point: [4914.0008208499439, 563.98457793124385]

World point: [36, 0, 0]
Actual Image point: [4010, 2073]
Calculated point: [4000.5696213734891, 2081.0042966664346]

World point: [0, 0, 0]
Actual Image point: [4826, 2141]
Calculated point: [4809.7130315564327, 2146.7310624716138]

World point: [0, 0, 72]
Actual Image point: [4642, 2800]
Calculated point: [4641.9905298563581, 2799.9064290859433]

wireframe is:

Zhang's method to calibrate mobile phone camera
Captured following planar images of checker board and gave as input to opencv implementation of zhang’s calibration method